## Slide 1: Part 10
Router traffic control
© O. Bonaventure, UCLouvain, 2023. Supplementary material for the Computer Networking : Principles, Protocols and Practice ebook, https://www.computer-networking.info

## Slide 2: Agenda
Congestion Control
  Principles
  Additive Increase/Multiplicative Decrease
  Explicit Congestion Notification
  Modern TCP Congestion control
  Router behavior

## Slide 3: Ressources
K. Nichols, V. Jacobson, Controlling Queue Delay, Commun. ACM, 55 (7) (2012), pp. 42-50, https://doi.org/10.1145/2209249.2209264
RFC8289
RFC8290
Toke Høiland-Jørgensen, Per Hurtig, Anna Brunstrom, The Good, the Bad and the WiFi: Modern AQMs in a residential setting, Computer Networks,Volume 89, 2015, https://doi.org/10.1016/j.comnet.2015.07.014

## Slide 4: Traffic control techniques
What are the techniques that a single router can use to provide different types of services to different applications ?
  First step : identify the applications that need to obtain each service type
  Second step : allocate network ressources to the different applications

## Slide 5: Router output port
Output link
Input link 1
Input link N
Classifier
IP packets
IP packets
IP packets with internal ID

## Slide 6: How would you implement a classifier ?
Per source classification ?
  IP address, IP prefix, TCP/UDP ports ?
Per destination classification ?
  IP address, IP prefix, TCP/UDP ports ?
Per application classification ?

## Slide 7: Buffer Acceptance
How to decide which packets can be accepted inside the buffer ?
Buffer
Classification
Input links
Output link

## Slide 8: Buffer Acceptance
The two key questions for a buffer acceptance algorithm
  When should the BA algorithm decide to discard a packet ?
  Which packet should be discarded ?

## Slide 9: Buffer Acceptance Algorithms
Tail drop
  Arrival (Packet p) : if isFull(Buffer) then discard p; else AddTail(Buffer, p);
What are its advantages and drawbacks ?

## Slide 10: The traffic control building blocks on router
Q[1]
Q[2]
Q[3]
Q[N]
Classification
Input links
Output link
Queuing strategy
Logical organisation of the
router's buffers
Scheduler
Chooses the packet to
be transmitted first on
the output link

## Slide 11: Priority scheduling
Flow 2, class B
Output buffer
Flow 1, class A
Flow 3, class B
Flow 4, class B
Flow N, class C
Class A
Class B
Class C
Packet transmission :
if (Queue(A) not empty)
serve Queue(A);
else
if (Queue(B) not empty)
serve Queue(B);
else
if (Queue(C) not empty)
serve Queue(C);
else ....

## Slide 12: Priority scheduling
With the priority scheduler, what is the ordering of the packets on the output link ?
A
D
B
E
F
C
High priority Queue
Medium Priority Queue
Low Priority Queue

## Slide 13: Round-Robin scheduling
Flow 2
Flow 1
Flow 3
Flow 4
Flow 5
Flow 1
Flow 2
Flow 3
Flow N
Scheduler :
F1
F2
F3
F4
FN

## Slide 14: Round robin
If the RR scheduler starts with queue1 and serves them in numerical order, what is the ordering of the packets on the output link ?
A
B
D
E
F
G
Queue 1
Queue 2
Queue 3

## Slide 15: Round-robin : example
F1
F2
F3
Flow2 (L=2)
Flow1(L=1)
Flow3 (L=1)
F1
F2
F3
Flow1 and Flow3 send packets of size 1
Flow 2 sends packets of size 2

## Slide 16: Example
F1
F2
F3
Flow2 (L=2)
Flow1(L=1)
Flow3 (L=1)
F1
F2
F3
Flow1 and Flow3 send packets of size 1
Flow 2 sends packets of size 2

## Slide 17: Round-Robin
Advantage
  Can provide fairness independently of the characteristics of the flows if flows use same packet size
Drawbacks
  Difficult to scale to a very large number of flows
  Unfair with different packet sizes

## Slide 18: Deficit Round-Robin
    associate counter d[i] to each queue
    increase d[i] by quantum every time queue[i] is visited
      if first_packet of queue[i] larger than d[i] { packet stays in queue[i]; }
      else { packet is transmitted on output link; d[i]=d[i]- packet length; if queue[i] is empty { d[i]=0; } }
Flow 2
Flow 1
Flow 3
Flow 4
Flow 5
Flow 1
Flow 2
Flow 3
Flow N
Scheduler :
F1
F2
F3
F4
FN

## Slide 19: Deficit Round-Robin : example
F1
F2
F3
Flow2 (L=2)
Flow1(L=1)
Flow3 (L=1)
F1
F2
F3
Flow1 and Flow3 send packets of size 1
Flow 2 sends packets of size 2

## Slide 20: Deficit Round robin
If the DRR scheduler starts with queue1 and serves them in numerical order, what is the ordering of the packets on the output link ?
A
B
D
F
G
Queue 1
Queue 2
Queue 3

## Slide 21: Weighted Round-Robin
Flow 2
Flow 1
Flow 3
Flow 4
Flow 5
Flow 1
Flow 2
Flow 3
Flow 5
Scheduler :
F1
F2
F3
F4
F5
F1
F2
F1
F1
Fraction of the bandwidth for each flow ?

## Slide 22: Weighted Round-Robin
A : 25%
B : 50%
C : 25%
Line rate
Line rate
Variable
B's share
A's share

## Slide 23: Weighted Round Robin
A : 25%
B : 50%
C : 25%
Input Traffic pattern
  A : 20%, regular
  B: 60%
  C: 50%

## Slide 24: Weighted Round Robin
What is the impact of a burst of traffic ?
A : 75%
B : 24%
C : 1%
Input Traffic pattern
  A : 20%, regular
  B: 24%
  C: 100%

## Slide 25: Schedulers and buffer acceptance
Which buffer acceptance strategy should be used with DRR or WDRR ?
  Can we identify the flow/queue that is causing congestion ?
  Which packet should be discarded ?

## Slide 26: Weighted Fair Queueing
What are the key characteristics of this scheduling technique ?
  What are its benefits compared with DRR ?

## Slide 27: Combining schedulers
Input Traffic pattern
  10% voice, regular
  30% data1
  60% data2
  50% data3
Data1
Data2
Data3
Voice
WFQ-like scheduler
Priority scheduler
66%
33%
1%
100%

## Slide 28: The traffic control building blocks QoS-enabled router
Q[1]
Q[2]
Q[3]
Q[N]
Classification
Shaping
Policing
Input links
Output link
Policer
Verifies whether the incoming
flow follows some rules
Classifier
Identifies the flow to which
the arriving packet belongs
Buffer acceptance
accepts or rejects an
incoming packet
Shaper
Delays flows which do not
follow some rules
Queuing strategy
Logical organisation of the
router's buffers
Scheduler
Chooses the packet to
be transmitted first on
the output link