## Slide 1: Part 11 Local Area Networks
© O. Bonaventure, UCLouvain, 2023. Supplementary material for the Computer Networking : Principles, Protocols and Practice ebook, https://www.computer-networking.info

## Slide 2: Agenda
Local Area Networks
  Ethernet
  IP over Ethernet
  Wi-Fi
Protocol stack

## Slide 4: First Ethernet
802.3
  10 Mbps
  Coaxial cable
Source: https://en.wikipedia.org/wiki/10BASE5

## Slide 5: Ethernet Addresses
Each Ethernet adapter has a unique address
Ethernet Address format
  48 bits addresses
    Source Address
    Destination address
      If high order bit is 0, host unicast address
  If high order bit is 1, host multicast address
    broadcast address = 111111..111
24 bits OUI
(adapter manufacturer)
24 bits
(identifier of adapter)
00
Notes: Ethernet addresses are usually printed as hexadecimal numbers, e.g.
alpha.infonet.fundp.ac.be (at 00:80:C8:FB:21:2B [ether] on eth0
cr1.info.fundp.ac.be at 00:50:BD:D0:E0:00 [ether] on eth0
backus.info.fundp.ac.be at 08:00:20:A6:62:8A [ether] on eth0
inspiron.infonet.fundp.ac.be at 00:50:04:8C:83:70 [ether] on eth0
corneille.info.fundp.ac.be at 00:20:AF:52:44:4B [ether] on eth0
See http://standards.ieee.org/regauth/oui/oui.txt for the list of allocations

## Slide 6: LAN-level multicast
Principle
  Two types of destination Ethernet addresses
    Physical addresses
    Logical addresses
      logical group of Ethernet destinations
  Transmission of multicast frames
  Reception of multicast frames
48 bits
0 : physical address (unicast)
1 : logical address (multicast)
OUI

## Slide 7: Ethernet Frames
DIX Format
  proposed by Digital, Intel and Xerox
Preamble
[8 bytes]
Destination address
Type
[2 bytes]
CRC [32 bits]
Source address
Data
[46-1500 bytes
Used to mark the beginning of the frame
Allows the receiver to synchronise its clock to the sender’s clock
Indication of the type of packet contained
inside the frame
Upper layer protocol must ensure that the payload of the Ethernet frame is
at least 46 bytes and at most 1500 bytes
Notes: This is the most widely used format, it is notably used to carry IP packets.

## Slide 8: Ethernet Service
An Ethernet network provides a connectionless unreliable service
Transmission modes
  unicast, multicast, broadcast
Even if in theory the Ethernet service is unreliable, a good Ethernet network should
  deliver frames to their destination with a very hig probability of delivery
  not reorder the transmitted frames
    reordering is obviously impossible on a bus

## Slide 9: Ethernet hub
A hub is a relay operating in the physical layer
Host A
Host B
Hub
Physical
Datalink
Datalink
Physical

## Slide 10: Larger Ethernet ?
Hub
Issue : maximum 51.2 microsec delay between any pair of stations
Hub
Hub
Hub

## Slide 11: Ethernet switch
A switch is a relay operating in the datalink layer
Host A
Host B
Switch
Physical
Phys.
Phys.
Datalink
Network
Network
Datalink
Physical

## Slide 12: The Ethernet zoo
10BASE5 | Thick coaxial cable, 500m
10BASE2 | Thin coaxial cable, 185m
10BASE-T | Two pairs of category 3+ UTP
10BASE-F | 10 Mb/s over optical fiber
100BASE-TX | Category 5 UTP or STP, 100 m maximum
100BASE-FX | Two multimode optical fiber, 2 km maximum
1000BASE-CX | Two pairs shielded twisted pair, 25m maximum
1000BASE-SX | Two multimode or single mode optical fibers with lasers
10 Gbps | optical fiber but also cat 6 twisted pair
40-100 Gbps | being developed, standard expected in 2010, 40Gbps one meter long for switch backplanes, 10 meters for copper cable and 100 meters for fiber optics
Notes: The 10 Gbps zoo is much larger than this, see e.g. http://en.wikipedia.org/wiki/10_gigabit_Ethernet

## Slide 13: Some Ethernet cables and plugs
Source : https://en.wikipedia.org/wiki/10BASE2, https://en.wikipedia.org/wiki/Ethernet_over_twisted_pair, https://en.wikipedia.org/wiki/Category_6_cable, https://en.wikipedia.org/wiki/Small_form-factor_pluggable_transceiver

## Slide 14: Ethernet Switch
Ethernet switch
  understands MAC addresses and filters frames based on their addresses
Address | Port
A | West
B | South
C | East
Eth : A
Eth : B
Eth : C
Src:A Dst:B
Notes: A good reference on Ethernet switches is
R. Seifert, J. Edwards, The All-New Switch Book, Wiley, 2008

## Slide 15: Frame processing
Arrival of frame F on port P
src=F.Source_Address;
dst=F.Destination_Address;
UpdateTable(src, P); // src heard on port P
if (dst==broadcast) || (dst is multicast)
{
for(Port p!=P) // forward all ports
  ForwardFrame(F,p);
}
else
{
if(dst isin AddressPortTable)
{
ForwardFrame(F,AddressPortTable(dst));
} else {
for(Port p!=P) // forward all ports
ForwardFrame(F,p);
}
}

## Slide 16: Network redundancy
Address | Port
A | West
B | South
C | East
Eth : A
Eth : B
Eth : C
Src:A Dst:C
Address | Port
A | North
B | South
C | East
Address | Port
A | West
B | South
C | North
S1
S2
S3

## Slide 17: Network redundancy (2)
Address | Port
Eth : A
Eth : B
Eth : C
Src:A Dst:C
Address | Port
Address | Port
S1
S2
S3

## Slide 18: Spanning tree
Switch 1
Switch 7
Switch 9
Switch 22
Switch 44
Switch 2
  Each switch has a unique identifier
  The switch with the lowest id is the root
  Disable frame forwarding on links that do not belong to the spanning tree

## Slide 19: Building spanning tree
  802.1d uses Bridge PDUs (BPDUs) containing
    Root ID : identifier of the current root switch
    Cost : Cost of the shortest path between the switch transmitting the BPDU and the root switch
    Transmitting ID : identifier of the switch that transmits the BPDU
  The BPDUs are sent by switches over their attached LANs as multicast frames but they are never forwarded
    switches that implement 802.1d listen to a special Ethernet multicast group

## Slide 20: Ordering for BPDUs
BPDUs can be strictly ordered
  BPDU1[R=R1,C=C1, T=T1] is better than BPDU2 [R=R2,C=C2, T=T2] if
    R1<R2
    R1=R2 and C1<C2
    R1=R2 and C1=C2 and T1<T2

## Slide 21: BPDU format
Simplified BPDU format
BPDU
Header
Root Id
Switch identifier
Root path cost
Protocol Identifier
Protocol version
Configuration BPDU or topology change
Flags
Identifier of the switch sending the BPDU
Port identifier : used when a switch has several ports attached to the same LAN
Current root identifier
Port identifier
Message age
Max age
Hello time
Forward delay

## Slide 22: 802.1d : Root behavior
  root switch sends regularly BPDUs on all its ports
    R=Root switch id, C=0, T= Current switch id(Root)
Bootstrap
      If a switch does not receive BPDUs, it considers itself as root

## Slide 23: Switch behaviour
On each port, switch parses all the received BPDUs and stores the best BPDU received on each port
  By comparing all received BPDUs, each switch can determine the root and its BPDU
Switch BPDU [Root, SwitchId, Cost, Port]
  Cost : Cost of best BPDU + cost of link
  Switch sends its BPDU on its designated ports

## Slide 24: 802.1d port states
802.1d port state based on received BPDUs
  Root port
    port on which best 802.1d BPDU received
  Designated port
    a port is designated if the switch's BPDU is better than the best BPDU received on this port
  Blocked port (only receives 802.1d BPDUs)
    A port is blocked is the switch's BPDU is worse than the best BPDU on this port

## Slide 25: Example network
    Switch 9 boots first
Switch 7
Switch 12
Switch 9
[R=9,C=0,T=9]
[R=9,C=0,T=9]
    Switch 12 boots
Switch 12
North: [R=9,C=0,T=9]
South : [R=9,C=0,T=9]
Cost:2
Cost:3
BPDU: [R=9,C=2,T=12]
Root
BPDU: [R=9,C=0,T=9]
Blocked
Designated
Designated

## Slide 26: Example network
Switch 7
Switch 12
Switch 9
[R=7,C=0,T=7]
    Switch 7 boots
Switch 12
North: [R=9,C=0,T=9]
South : [R=9,C=0,T=9]
Cost:2
Cost:3
BPDU: [R=9,C=2,T=12]
Root
BPDU: [R=9,C=0,T=9]
Blocked
Designated
Designated
Switch 9
North: -
South : -
[R=7,C=0,T=7]
[R=7,C=2,T=12]
[R=7,C=0,T=7]
[R=7,C=2,T=9]
Root
[R=7,C=2,T=12]
Designated
[R=7,C=2,T=12]
[R=7,C=2,T=9]
[R=7,C=2,T=9]

## Slide 27: Port activity
Two possible port activities
  Active port
    Participates to data frame forwarding
    Port used for address/port table
  Inactive port
    The switch does not listen to frames neither forward frames on this port

## Slide 28: Port states and activity
 | Receive BPDUs | Transmit BPDUs
Blocked | yes | no
Root | yes | no
Designated | yes | yes
 | Learn Addresses | Forward Data Frames
Inactive | no | no
Active | yes | yes

## Slide 29: Behaviour of the ports
 | Receive BPDUs | Transmit BPDUs | Learn Addresses | Forward Data Frames
Blocking | yes | no | no | no
Listening | yes | yes | no | no
Learning | yes | yes | yes | no
Forwarding | yes | yes | yes | yes

## Slide 30: Influencing Spanning Tree
Switch identifiers
  High order bits : configurable
  Low order bits : unique identifier
Link costs : Cost = 1000 / bandwidth
Bandwidth | Recommended link cost range | Recommended link cost value
10 Mbps | 50-600 | 100
100 Mbps | 10-60 | 19
1000 Mbps | 3-10 | 4

## Slide 31: Impact of failures
  Failure (power-off) of the root switch
    A new root needs to be elected
  Failure of a designated switch
    Another switch should takeover
  Failure of a link
    Network must be redundant
  Failure of a link that disconnects the network

## Slide 32: Dealing with failures
Failure detection mechanisms
  Root switch sends BPDU every Hello sec
  Designated switches send own BPDUs
  BPDUs stored in the switches age and are removed when they timeout
    This might cause a recomputation of the tree

## Slide 33: Another example
Switch 7
Switch 12
Switch 9
Switch 3
Switch 11
Designated
Designated
Root
Root
[R=3,C=0,T=3]
[R=3,C=0,T=3]
[R=3,C=1,T=9]
[R=3,C=1,T=12]
Designated
Designated
[R=3,C=1,T=9]
Root
[R=3,C=2,T=7]
[R=3,C=2,T=11]
Root
Blocked
Designated
Blocked

## Slide 34: A failure
Switch 7
Switch 12
Switch 9
Switch 3
Switch 11
Designated
Designated
Root
Root
[R=3,C=0,T=3]
[R=3,C=1,T=12]
Designated
Designated
[R=3,C=1,T=9]
Root
[R=3,C=2,T=7]
[R=3,C=2,T=11]
Root
Blocked
Designated
Blocked
Timeout !!!
Root
Designated
[R=3,C=3,T=9]
[R=3,C=3,T=11]
Root
Designated
Root
Blocked

## Slide 35: Spanning Tree check list
In a network composed of Ethernet switches
  There is only one root switch
A given Ethernet switch
  Has only one root port
Point to point links are either
  Designated -> Root
  Designated->Blocked

## Slide 36: Recomputing the spanning tree
Failure notification mechanism
  When a switch detects important failure, it sends a topology change BPDU to Root
    Root broadcasts TC
    All switches stop forwarding data frames and recompute spanning tree

## Slide 37: Congestion in Ethernet switches
  How to solve this problem inside Ethernet ?
      Add buffers to switches and let TCP work
      Develop a new flow control mechanism inside MAC layer
        Pause frame to slowdown transmission
S1
S2
Server
Client
10 Gbps
Ethernet (100 Mbps)

## Slide 38: Ethernet flow control
  PAUSE frame indicates how much time the upstream should wait before transmitting next frame
S1
server
Client
FastEthernet
(100 Mbps)
Ethernet
(10 Mbps)
PAUSE [2msec]
Frame1 [10000 bits]
Frame3 [10000 bits]
Frame2 [10000 bits]
100 nsec
Frame1 [10000 bits]
1 microsec
Frame2 [10000 bits]
Sender blocked

## Slide 39: Virtual LANs
Allows to build several logical networks on top of a single physical network
S
A
B
C
D
F
E
Each port on each switch is associated to a particular VLAN
All the hosts that reside on the same VLAN can exchange Ethernet frames
A host on VLAN1 cannot send an Ethernet frame towards another host that belongs to VLAN2
Broadcast and multicast frames are only sent to the members of the VLAN
VLAN1 : A,E,F
VLAN2 : B,C,D

## Slide 40: VLANs in campus networks
S1
A
B
C
D
F
E
VLAN1 : A,E,F
VLAN2 : B,C,D
S2
Possible solutions
Place on each switch a table that maps each MAC address on a VLAN id
    difficult to manage this table
Change frame format used on inter-switch links to include a VLAN identifier
new header added by first switch
new header removed by last switch
Notes: See
[IEEE802Q] "IEEE Standards for Local and Metropolitan Area
Networks: Virtual Bridged Local Area Networks", Draft Standard, P802.1Q/D9, February 20, 1998.

## Slide 41: VLAN frame format
Used on inter-switch links
  Can also be used by trusted hosts (e.g. servers) or routers
Destination
Address
Source
Address
Identifies the frame as containing VLANtag
Tag control information contains two types of information :
- VLAN identifier (12 bits) : up to 4094 different VLANs can be defined
- Priority (3 bits) : indicates the importance of the frame and can be used by switches to provide a better service for some frames (e.g. Voice)
Type
CRC [32 bits]
Payload
VLAN Protocol Id 0x8100
Tag Control Info

## Slide 42: Agenda
Local Area Networks
  Ethernet
  IP over Ethernet
  Wi-Fi
Protocol stack

## Slide 43: Datalink layer service
Unreliable connectionless service
Each device is identified by a 48 bits MAC address
To send a frame using the datalink layer service, the network layer must know the MAC address of the destination
  send(destination, data)

## Slide 44: IPv4 subnet
A subnet gathers hosts and routers that can directly exchange frames without passing through an intermediate router
R
192.0.2.0/24
Ethernet: AA
192.0.2.9/24
Ethernet: BB
192.0.2.21/24
Ethernet: CC
192.0.2.33/24
Ethernet: DD
192.0.2.1/24

## Slide 45: IPv4 subnet
Questions
  What are the smallest and largest numbered addresses of the 192.0.2.0/26 subnet ?
  What are the smallest and largest numbered addresses of the 198.51.100.160/27 subnet ?

## Slide 46: IPv4 over Ethernet
Initially manual configuration of
  IP address, subnet, router, DNS resolver
  Autoconfiguration now handled by DHCP
Address Resolution Protocol (ARP) to find the Ethernet address associated to an IP addr

## Slide 47: Address Resolution Protocol
192.0.2.11
Eth : A
192.0.2.11 wants to send a packet to 192.10.2.33
ARP request 192.0.2.33 ? sent to Ethernet broadcast address
1
2
3
192.0.2.22
Eth : E
192.0.2.33
Eth : C
ARP reply 192.0.2.33 is reachable via Ethernet Add : C
192.0.2.11
Eth : A
192.0.2.22
Eth : E
192.0.2.33
Eth : C
192.0.2.11
Eth : A
192.0.2.22
Eth : E
192.0.2.33
Eth : C
Notes: The transmission of IPv6 packets over Ethernet is defined in :
M. Crawford, Transmission of IPv6 Packets over Ethernet Networks, RFC2464, December 1998
Note that in contrast with ARP used by IPv4, ICMPv6 neighbour solicitation messages are sent to a multicast ethernet address and not to the broadcast ethernet address. This implies that only the IPv6 enabled hosts on the LAN will receive the ICMPv6 message.

## Slide 48: IPv6 subnet
A subnet gathers hosts and routers that can directly exchange frames without passing through an intermediate router
R
2001:db8:1234:5678::/64
2001:db8:1234:5678::AA
2001:db8:1234:5678::BB
2001:db8:1234:5678::CC
2001:db8:1234:5678::1

## Slide 49: Why using subnets ?
Improves network scalability
  Routers maintain routes per subnet or per groups of subnets
Allows to group hosts together
  Students in different subnet than staff
  Servers in different subnet than laptops
What is the size in bits of the IPv6 subnet that your ISP allocates you at home ?

## Slide 50: Neighbour discovery
IPv6: 1080:0:0:0:8::A
Eth : A
1080:0:0:0:8::A wants to send a packet to 1080:0:0:0:8::C
Neighbour solicitation: Addr Eth 1080:0:0:0:8::C ? sent to IPv6 multicast address
1
2
3
IPv6: 1080:0:0:0:8::E
Eth : E
Ipv6: 1080:0:0:0:8::C
Eth : C
Ipv6: 1080:0:0:0:8::C
Eth : C
IPv6: 1080:0:0:0:8::E
Eth : E
IPv6: 1080:0:0:0:8::A
Eth : A
Neighbour advertisement: 1080:0:0:0:8::C is reachable via Ethernet Add : C
Ipv6: 1080:0:0:0:8::C
Eth : C
IPv6: 1080:0:0:0:8::E
Eth : E
IPv6: 1080:0:0:0:8::A
Eth : A
Notes: The transmission of IPv6 packets over Ethernet is defined in :
M. Crawford, Transmission of IPv6 Packets over Ethernet Networks, RFC2464, December 1998
Note that in contrast with ARP used by IPv4, ICMPv6 neighbour solicitation messages are sent to a multicast ethernet address and not to the broadcast ethernet address. This implies that only the IPv6 enabled hosts on the LAN will receive the ICMPv6 message.

## Slide 51: Autoconfiguration
What happens when a host boots ?
    Use Link-local IPv6 address (FE80::/64)
      Each interface has a link-local IPv6 address
      But another node might have chosen the same address !
R
Ethernet : 0800:200C:417A FE80::M64(800:200C:417A)
Address is valid if nobody answers
ICMPv6 Neighbour sollicitation
Notes: This utilisation of ICMPv6 Neighbour solicitation is called Duplicate Address Detection. It is used everytime a host obtains a new IPv6 address and is required to ensure that a host is not using the same IPv6 address as another host on the same LAN.

## Slide 52: IPv6 link-local addresses
Used by devices on same LAN to exchange IPv6 packets when they don't have/need globally routable address
    Each host/router must generate one link local address for each of its interfaces
  Each IPv6 host uses several IPv6 addresses
interface ID
128 bits
10 bits
54 bits
64 bits
FE80
0000000000.....00000000000
Notes: Site-local addresses were defined in the first IPv6 specifications, but they are now deprecated and should not be used.
Recently “private” addresses have been defined as Unique Local IPv6 Addresses as a way to allow entreprise to obtain IPv6 addresses without being forced to request them from providers or RIRs.
The way to choose such a ULA prefix is defined in :
R. Hinden, B. Haberman, Unique Local IPv6 Unicast Addresses, RFC4193, October 2005
Recently, the case for a registration of such addresses has been proposed, see :
R. Hinden, G. Huston, T. Narten, Centrally Assigned Unique Local IPv6 Unicast Addresses, internet draft, <draft-ietf-ipv6-ula-central-02.txt>, work in progress, June 2007
See also
http://www.ripe.net/ripe/policies/proposals/2007-05.html -

## Slide 53: Global IPv6 address
How to obtain the IPv6 prefix of the subnet ?
  Wait for router advertisements
  Solicit router advertisement
R
ICMPv6 : Router Solicitation
IPv6 Src: FE80::M64(800:200C:417A)
IPv6 Dest: FF02::2
Ethernet : 0800:200C:417A FE80::M64(800:200C:417A)

## Slide 54: Router advertisements
Type:134 Code : 0
Checksum
Retrans Timer
Ver Tclass
Flow Label
58 255
Router IPv6 address
(link local)
Payload Length
FF02::1
(all nodes)
CurHLim
Router lifetime
Maximum hop limit to avoid spoofed packets from outside LAN
M O Res
Reachable Time
Options
Value of hop limit to be used by hosts when sending IPv6 packets
The lifetime associated with the default router in units of seconds. 0 is the router sending the advertisement is not a default router.
The time, in milliseconds, that a node assumes a neighbour is reachable after having received a reachability confirmation.
The time, in milliseconds, between retransmitted Neighbor Solicitation messages.
MTU to be used on the LAN
Prefixes to be used on the LAN
Notes: When the M bit is set to true, this indicates that IPv6 addresses should be obtained from DHCPv6
When the O bit is set to true, this indicates that the hosts can obtain additional information (e.g. address of DNS resolver) from DHCPv6
The router advertisements messages can also be sent in unicast in response to solicitations from hosts. A host can obtain a router advertisement by sending a router solicitation which is an ICMPv6 message containing only the router solicitation message (type 133).

## Slide 55: RA options
Format of the options
MTU option
Prefix option
Type Length
Options
Options (cont.)
Type : 5 Length:1
Reserved
MTU
Type : 3 Length:4
PreLen
L A Res.
Valid Lifetime
Preferred Lifetime
Reserved2
IPv6 prefix
Number of bits in IPv6 prefix that identify subnet
The validity period of the prefix in seconds
The duration in seconds that addresses generated from the prefix via stateless address autoconfiguration remain preferred.
Notes: The two L and A bits are defined as follows :
L 1-bit on-link flag. When set, indicates that this
prefix can be used for on-link determination. When
not set the advertisement makes no statement about
on-link or off-link properties of the prefix. In
other words, if the L flag is not set a host MUST
NOT conclude that an address derived from the
prefix is off-link. That is, it MUST NOT update a
previous indication that the address is on-link.
A 1-bit autonomous address-configuration flag. When
set indicates that this prefix can be used for
stateless address configuration.
Other options have been defined for the router advertisements. For example, the RDNSS option defined in
J. Jeong, S. Park, L. Beloeil, S. Madanapalli, IPv6 Router Advertisement Option for DNS Configuration, RFC 5006, Sept. 2007
allows a router to advertise the IPv6 address of the DNS resolver to be used by hosts on the LAN.

## Slide 56: ICMPv6 Neighbour Discovery
Neighbour solicitation
Neighbour advertisement
Type : 135 Code:0
Checksum
Target IPv6 Address
Reserved
The IPv6 address for which the link-layer (e.g. Ethernet) address is needed.
May also contain an optional field with the link-layer (e.g. Ethernet) address of the sender.
Type : 136 Code:0
Checksum
Target IPv6 Address
R S O Reserved
Target link layer Address
The IPv6 and link-layer addresses
R : true if node is a router
S : true if answers to a neighbour solicitation
Notes: The ICMPv6 neighbour discovery messages are sent with HopLimit=255
The role of the R, S and O flags is described as follows in RFC4861
R Router flag. When set, the R-bit indicates that
the sender is a router. The R-bit is used by
Neighbor Unreachability Detection to detect a
router that changes to a host.
S Solicited flag. When set, the S-bit indicates that
the advertisement was sent in response to a
Neighbor Solicitation from the Destination address.
The S-bit is used as a reachability confirmation
for Neighbor Unreachability Detection. It MUST NOT
be set in multicast advertisements or in
unsolicited unicast advertisements.
O Override flag. When set, the O-bit indicates that
the advertisement should override an existing cache
entry and update the cached link-layer address.
When it is not set the advertisement will not
update a cached link-layer address though it will
update an existing Neighbor Cache entry for which
no link-layer address is known. It SHOULD NOT be
set in solicited advertisements for anycast
addresses and in solicited proxy advertisements.
It SHOULD be set in other solicited advertisements
and in unsolicited advertisements.

## Slide 57: Global IPv6 address
  IPv6 addresses are allocated for limited lifetime
    This allows IPv6 to easily support renumbering
R
ICMPv6 : Router Advertisement
IPv6 Src: FE80::M64(EthernetR)
IPv6 Dest: FF02::1
IPv6 Prefix = 2001:6a8:1100::/48
Prefix lifetime
Ethernet : 0800:200C:417A FE80::M64(800:200C:417A)
Notes: IPv6 is supposed to easily support renumbering and IPv6 router advertisements are one of the ways to perform this renumbering by allowing hosts to update their IPv6 addresses upon
reception of new router advertisement messages. However, in practice renumbering an IPv6 network is not easily because IPv6 addresses are manually encoded in too many
configuration files, see e.g. :
F. Baker, E. Lear, R. Droms, Procedures for Renumbering an IPv6 Network without a Flag Day, RFC4192, 2005

## Slide 58: Privacy concerns
Autoconfigured IPv6 addresses contain the MAC address of the hosts
How to maintain privacy with IPv6 ?
  Use DHCPv6 and configure server to never reallocate the same IPv6 address
  Allow hosts to use random host ids in lower 64 bits of their IPv6 address
    algorithms have been implemented to generate such random host ids on nodes with and without stable storage
Notes: This extension to support privacy-aware IPv6 addresses is defined in
T. Narten, R. Draves, S. Krishnan, Privacy Extensions for Stateless Address Autoconfiguration in IPv6, RFC4941, Sept. 2007

## Slide 59: IPv6 over Ethernet
Eth : B
ND table
Empty
Eth : C
ND table
Empty
Eth : A
ND table
Empty
R1
Eth : R1-West
Eth : R1-East
ND table
Empty
H1
S2
R2
Hub
Router
Switch
Router
Eth : F
ND table
Empty
Eth : R2-West
Eth : R2-East
ND table
Empty
p1::AA/64 East
::/0 via p1::11
p1::CC/64
::/0 via p1::11
p1::11/64 West
p2::11/64 East
p3::/64 via p2::22
p1::/64 via p2::11
p2::22/64 West
p3::22/64 East
p2::BB/64
::/0 via p2::22
p3::FF/64
ND ? p1::CC
ND p1::CC=C
p1::AA sends a packet to p1::CC
p1::CC == C
IP: src=p1::AA dest = p1::CC
Ethernet src=A dest = C

## Slide 60: IPv6 over Ethernet
Eth : C
ND table
Empty
Eth : A
ND table
Empty
R1
Eth : R1-West
Eth : R1-East
ND table
Empty
H1
S2
R2
Hub
Router
Switch
Router
Eth : F
ND table
Empty
Eth : R2-West
Eth : R2-East
ND table
Empty
p1::AA/64 East
::/0 via p1::11
p1::CC/64
::/0 via p1::11
p1::11/64 West
p2::11/64 East
p3::/64 via p2::22
p1::/64 via p2::11
p2::22/64 West
p3::22/64 East
p3::FF/64
p1::CC sends a packet to p3::FF
ND ? p1::11
p1::CC == R1-West
IP: p1::CC->p3::FF
Eth: C -> R1-West
ND ? p2::22
ND p1::11=R1-West
p2::22 == R2-West
IP: p1::CC->p3::FF
Eth: R1-East -> R2-West
ND p2::22=R2-West

## Slide 61: Issues with IPv6 subnet
How can a host learn the MAC address of the destination based on its IPv6 address ?
R
2001:db8:1234:5678::/64
2001:db8:1234:5678::AA
2001:db8:1234:5678::BB
2001:db8:1234:5678::CC
2001:db8:1234:5678::1

## Slide 62: DHCPv6 versus SLAAC
What are the pros and cons and these solutions ?

## Slide 63: Agenda
Local Area Networks
  Ethernet
  IP over Ethernet
  Wi-Fi
Protocol stack

## Slide 64: How to regulate transmission of frames ?
Medium Access Control algorithms

## Slide 65: ALOHA
N=1;
while ( N<= max) do
send frame;
wait for ack on return channel or timeout:
if ack on return channel
exit while;
else
/* timeout */
/* retransmission is needed */
wait for random time;
N=N+1;
end do
/* too many attempts */

## Slide 66: CSMA
N=1;
while ( N<= max) do
wait until channel becomes free;
send frame immediately;
wait for ack or timeout:
if ack received
exit while;
else
/* timeout */
/* retransmission is needed */
N=N+1;
end do
/* too many attempts */

## Slide 67: CSMA/CA
A MAC for wireless networks
Improvements to CSMA
  Initial delay to transmit (EIFS)
  Min. delay between frames (DIFS)
  Delay between frame and ack (SIFS)

## Slide 68: CSMA/CA : receiver
While (true)
{
Wait for data frame;
if not(duplicate)
{ deliver (frame) }
wait during SIFS;
send ack (frame) ;
}

## Slide 69: CSMA/CA : sender
N=1;
while ( N<= max) do
if (previous frame corrupted)
{ wait until channel free during t>=EIFS; }
else
{ wait until endofframe;
wait until channel free during t>=DIFS; }
send data frame ;
wait for ack or timeout:
if ack received
exit while;
else
/* timeout retransmission is needed */
N=N+1;
end do
/* too many attempts */

## Slide 70: Example
A
B
C
DIFS
Data frame
Busy
SIFS
ACK frame
DIFS
Data frame

## Slide 71: Collisions
A
B
C
DIFS
DIFS
Data frame
Busy
Data frame
Busy
Timeout
Timeout
Data frame
Busy
Data frame

## Slide 72: CSMA/CA : sender
N=1;
while ( N<= max) do
if (previous frame corruped)
{ wait until channel free during t>=EIFS; }
else
{ wait until endofframe;
wait until channel free during t>=DIFS; }
backoff_time = int(random[0,min(255,7*2N-1)])*T
wait(channel free during backoff_time)
send data frame ;
  wait for ack or timeout:
if ack received
exit while;
else /* timeout retransmission is needed */
N=N+1; }
end do
Notes: The value T is defined in the standard, but a detailed discussion of this value is outside the scope of this presentation.

## Slide 73: Backoff
A
B
C
DIFS
DIFS
Backoff[0,7]
Backoff[0,7]
Busy
Channel busy!
Data frame
Data frame
SIFS
Ack frame
Remaining backoff

## Slide 74: Hidden station problem
A
B
C
Only hears B, not C
Hears B, but not A
Hears A and C

## Slide 75: Hidden station
How to solve it ?
  Sender reserves time slot
  Receiver confirms the time reservation

## Slide 76: RTS/CTS
A
B
C
DIFS+Backoff
Busy[ 100microsec+
SIFS+
CTS+
SIFS+
ACK
]
RTS [100 microsec]
SIFS
CTS[100microsec]
Data [100 microsec]
SIFS
ACK frame
SIFS

## Slide 77: The WiFi zoo
Standard | Frequency | Typical throughput | Raw bandwidth | Range in/out (m)
802 .11 | 2.4 GHz | 0.9 Mbps | 2 Mbps | 20 / 100
802 .11a | 5 GHz | 23 Mbps | 54 Mbps | 35 / 120
802 .11b | 2.4 GHz | 4.3 Mbps | 11 Mbps | 38 / 140
802 .11g | 2.4 GHz | 19 Mbps | 54 Mbps | 38 / 140
802 .11n | 2.4 / 5 GHz | 74 Mbps | up to 600 Mbps | 70 / 250
Source http://en.wikipedia.org/wiki/IEEE_802.11n

## Slide 78: Home networks
  A WLAN can interfere with the neighbour’s WLAN

## Slide 79: Enterprise networks

## Slide 80: WiFi channel frequencies
WiFi standards operate on several channels
  Usually about a dozen channels
Why multiple channels ?
  Some channels may have interference
  Some frequencies reserved for specific usage
  Allows frequency reuse when there are multiple WiFi networks in the same area
    Unfortunately, many home access points operate by default on the same channel
Notes: Example
802.11b channel frequencies
Channel Lower frequency Central frequency Upper frequency
1 2.401 2.412 2.423
2 2.404 2.417 2.428
3 2.411 2.422 2.433
4 2.416 2.427 2.438
5 2.421 2.432 2.443
6 2.426 2.437 2.448
7 2.431 2.442 2.453
8 2.436 2.447 2.458
9 2.441 2.452 2.463
10 2.446 2.457 2.468
11 2.451 2.462 2.473

## Slide 81: Enterprise networks
What could be done to improve the performance of WLANs ?
  Reduce interference as much as possible
        Recent deployments rely on centralised controllers and thin access points

## Slide 82: 802.11 frame format
Frame control
[2 bytes]
Duration/Id
[2 bytes]
Address 2 [6 bytes]
Address 1 [6 bytes]
Standard header
- Protocol version [2 bits] : current version 0
- Type [2 bits] : control / data / management frame
- Subtype [2 bits] : specific subtype of frame
- to DS [1 bit] : frame is sent to distribution system
- from DS [1 bit] : frame is from distribution system
- more fragment [1 bit] : used when packets are fragmented
- Retry [1 bit] : retransmission
- Power Management [1 bit] : used for power management fct
- More data [1 bit] : indicates that there are other frames for this station at the access point
- WEP [1 bit] : 1 if frame has been encrypted with WEP
- order [1 bit] : for strictly ordered class
Address 3 [6 bytes]
Sequence control [2 bytes]
Frame body [0-2312 bytes]
Frame Check Sequence
Sequence number
- 12 bits frame sequence number
- 4 bits fragment number

## Slide 83: 802.11 control frames
Frame control
[2 bytes]
Duration
[2 bytes]
Receiver address [6 bytes]
Frame Check Sequence
Frame control
[2 bytes]
Duration
[2 bytes]
Receiver address [6 bytes]
Frame Check Sequence
Transmitter address [6 bytes]
Frame control
[2 bytes]
Duration
[2 bytes]
Receiver address [6 bytes]
Frame Check Sequence
ACK frame
RTS frame
CTS frame

## Slide 84: IP over 802.11
Frame control
Duration/Id
[2 bytes]
Address 2 [6 bytes]
Address 1 [6 bytes]
Address 3 [6 bytes]
Sequence control [2 bytes]
IP packet
Frame Check Sequence
LLC/SNAP
0x800
LLC/SNAP
- 4 bytes header
EtherType
- 0x800 for IP, 0x86DD for IPv6

## Slide 85: Agenda
Local Area Networks
  Ethernet
  IP over Ethernet
  Wi-Fi
Protocol stack

## Slide 86: Protocol stack Physical layer
Unit of information : bit
Reliability
  transmission errors
  creation/suppression of bits
Physical
Physical
Physical

## Slide 87: Protocol stack Datalink layer
Unit of information
  Frame
Services
  Unreliable connectionless
  Reliable connection-oriented
Physical
Physical
Datalink
Datalink
Physical
Datalink
Frame

## Slide 88: Protocol stack Network layer
Unit of information
  packet
Services
  Unreliable connectionless
Organisation
  Datagram, virtual circuits
Physical
Physical
Datalink
Datalink
Network
Network
Physical
Datalink
Network
Packet

## Slide 89: Protocol stack Transport layer
Unit of information
  segment
Services
  Unreliable connectionless
  Reliable connection-oriented
Physical
Physical
Datalink
Datalink
Network
Network
Physical
Datalink
Network
Transport
Transport
Segment

## Slide 90: Protocol stack Application layer
Physical
Physical
Datalink
Datalink
Network
Network
Physical
Datalink
Network
Transport
Transport
Application
Application
SDU
Layer1
Layer2
Layer3
Layer4

## Slide 91: OSI Reference Model
Physical
Physical
Datalink
Datalink
Network
Network
Physical
Datalink
Network
Transport
Transport
Application
Application
SDU
Session
Session
Presentation
Presentation
Layer7