## Slide 1: Part 3
Reliable data transfer over an unreliable network
© O. Bonaventure, UCLouvain, 2023. Supplementary material for the Computer Networking : Principles, Protocols and Practice ebook, https://www.computer-networking.info

## Slide 2: Agenda
Reliable data transfer over a reliable network
How unreliable is the Internet ?
Reliable data transfer techniques
  The Alternating Bit Protocol
  Go-Back-N
  Selective repeat

## Slide 3: How to reliably transfer data ?
Hypothesis
  Internet is fully reliable
A B
Data.request(a)
segment(a)
Data.ind(a)
Data.request(b)
segment(b)
Data.ind(b)
Data.request(c)
segment(c)
Data.ind(c)

## Slide 4: Does this always work ?

## Slide 5: Question
What do we need to add to our “reliable” transfer to allow a datacenter to send data to an Internet of Things device without overflow ?

## Slide 6: Finite State Machine
Sender
Receiver

## Slide 7: Control and data segments
A B
Data.req(b)
C(OK)
Data.ind(a)
D(a)
Data.req(a)
D(b)
Data.ind(b)
C(OK)
Payload
Header
Trailer
Round trip time (rtt)

## Slide 8: Question
Two hosts are connected with a 1 Gbps (10^9 bits/sec) network. It takes one msec to deliver a 1000 bits segment from host A to host B. What is the bandwidth that this protocol will achieve (in bits per second) ?

## Slide 9: Agenda
Reliable data transfer over a reliable network
How unreliable is the Internet ?
Reliable data transfer techniques
  The Alternating Bit Protocol
  Go-Back-N
  Selective repeat

## Slide 10: The network is imperfect
What can happen to a packet sent over the Internet ?
Packet reaches destination
Packet can suffer transmission errors
  Packet contents can be corrupted
  Links have typically Bit Error Rates of 10-8 to 10-11
  Wireless suffers from more errors than cable and fiber
Packet can be dropped before reaching destination
Packet can be delayed

## Slide 11: Measuring Internet performance

## Slide 12: Internet packet losses
What can explain these packet loss ratios ?
Based on data extracted by François Michel from measurementlab’s big query

## Slide 13: Measuring Internet performance (2)

## Slide 14: Internet performance in Wallonia
Broadband access at 30 Mbps or better

## Slide 15: Initiative Amélie Améliorer Internet partout
Objectif
  L’initiative Amélie vise à mettre sur pied une équipe d’étudiant.e.s bénévoles afin de proposer un service de diagnostic Internet d’habitations privées. L’objectif est d’aider les habitants à améliorer la qualité de leur connexion Internet sans nécessairement changer d’offre ou de fournisseur
Mise en oeuvre
  Formation à l’analyse des performances en utilisant des outils adaptés et au diagnostic des facteurs qui réduisent les performances
  Coaching par des chercheurs qui améliorent Internet et des étudiant.e.s de Master

## Slide 16: Agenda
Reliable data transfer over a reliable network
How unreliable is the Internet ?
Reliable data transfer techniques
  The Alternating Bit Protocol
  Go-Back-N
  Selective repeat

## Slide 17: How to deal with transmission errors ?
The receiver must be able to detect that the content of a segment has been modified
  Checksum, CRC

## Slide 18: Question
How should a host react when it receives a data segment with an incorrect checksum ?

## Slide 19: Coping with errors
A B
Data.req(b)
C(OK)
Data.ind(a)
D(a)
Data.req(a)
D(b)
D(b)
Data.ind(b)
start timer
timer expires
What do you think of this protocol ?

## Slide 20: Coping with errors
A B
Data.req(b)
C(OK)
Data.ind(a)
D(a)
Data.req(a)
D(b)
D(b)
Data.ind(b)
start timer
timer expires
C(OK)
Data.ind(b)
Is this a problem for you ?

## Slide 21: A better approach
Key ideas
  Identify each data segment with a sequence number
    allows to prevent duplication
    one bit is sufficient
  Indicate the sequence number of the last data segment in the acknowledgement

## Slide 22: Alternating Bit Protocol : basics
A B
Data.req(b)
C(OK0)
Data.ind(a)
D(0,a)
Data.req(a)
D(1,b)
Data.ind(b)
C(OK1)
Data.ind(c)
D(0,c)
Data.req(c)
C(OK0)

## Slide 23: Alternating Bit Protocol : reaction to losses
A B
Data.req(b)
C(OK0)
Data.ind(a)
D(0,a)
Data.req(a)
D(1,b)
Data.ind(b)
Data.req(c)
Lost
D(0,c)
C(OK1)
D(1,b) recvd
Retransmission timer
Data.ind(c)
D(0,c)
C(OK0)

## Slide 24: Alternating Bit Protocol : early timer
A B
Data.req(b)
C(OK0)
Data.ind(a)
D(0,a)
Data.req(a)
Duplicate detected
Which ack to send ?
D(1,b)
Retransmission timer
D(1,b)
Data.ind(b)
Data.req(c)
C(OK1)
D(1,b) recvd
C(OK1)
D(1,b) recvd
Data.ind(c)
D(0,c)

## Slide 25: Question
Do we need to place a checksum/CRC inside the control segments ?

## Slide 26: Alternating Bit Protocol : unprotected control segments
A B
Data.req(b)
C(OK0)
Data.ind(a)
D(0,a)
Data.req(a)
Duplicate detected
D(1,b)
Retransmission timer
D(1,b)
Data.ind(b)
Data.req(c)
Lost
D(0,c)
C(OK1)
D(1,b) recvd
C(OK0)
D(0,c) recvd
Data.req(d)
D(1,d)
C(OK1)
Undetected transmission error
Duplicate detected

## Slide 27: Alternating bit : sender

## Slide 28: Alternating Bit : Receiver

## Slide 29: Alternating Bit Protocol
A B
Data.req(b)
C(OK0)
Data.ind(a)
D(0,a)
Data.req(a)
Duplicate detected
D(1,b)
Retransmission timer
D(1,b)
Data.ind(b)
Data.req(c)
Lost
D(0,c)
C(OK1)
D(1,b) recvd
C(OK0)
D(0,c) recvd
Transmission error
Data.req(d)
D(1,d)
C(OK0)
Duplicate detected

## Slide 30: Alternating Bit Protocol
Advantages
  Simple to implement
  Reliable data transfer
Drawback
  Performance
    only one segment per round-trip-time

## Slide 31: Agenda
Reliable data transfer over a reliable network
How unreliable is the Internet ?
Reliable data transfer techniques
  The Alternating Bit Protocol
  Go-Back-N
  Selective repeat

## Slide 32: Pipelining
Key ideas
  Allow the sender to send several segments without having an explicit ack
  Sender stores unacked segments in a buffer called the sending window to be able to retransmit them

## Slide 33: Pipelining
How many segments can A send ?
A B
Data.ind(a)
Data.req(a)
...
D(0,a)
...
D(4,e)
Data.req(b)
Data.req(e)
Data.ind(e)

## Slide 34: The sending window
Buffer managed by a sender
  Stores segments sent but not yet acknowledged
    Content of sending window can be retransmitted if needed
Sending window size limits the number of segments that a host can sent without acknowledgements

## Slide 35: Pipelining example
A B
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
Data.req(a)
Data.ind(a)
D(0,a)
0 1 2 3 4 5 6 7 8
Data.req(b)
Data.ind(b)
D(1,b)
0 1 2 3 4 5 6 7 8
Data.req(c)
Data.ind(c)
D(2,c)
C(OK0)
C(OK1)
C(OK2)
0 1 2 3 4 5 6 7 8
Data.req(d)
Data.ind(d)
D(3,d)
0 1 2 3 4 5 6 7 8
Data.req(e)
D(4,e)
Sending window
Sending window must be larger than bandwidth x round-trip-time to fully use network

## Slide 36: Sequence numbers are finite and reused
A B
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3
Data.req(a)
Data.ind(a)
D(0,a)
Data.req(b)
Data.ind(b)
D(1,b)
Data.req(c)
Data.ind(c)
D(2,c)
C(OK0)
C(OK1)
C(OK2)
Data.req(d)
Data.ind(d)
D(3,d)
Data.req(e)
D(0,e)
Sending window
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3

## Slide 37: How to deal with losses ?
Go-back-n
  Sender stores transmitted segments in sending window to be able to retransmit them if needed
  Simple receiver, accepts only in-sequence segments. If a segment is errored, sender retransmits all unacked segments
Selective repeat
  Sender stores transmitted segments in sending window to be able to retransmit them if needed
  Advanced receiver, stores out-of-sequence segments. If a segment is errored, sender only retransmits the errored segments

## Slide 38: Go-back-n
A B
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3
Data.req(e)
Data.req(a)
Data.ind(a)
D(0,a)
Data.req(c)
D(2,c)
C(OK,0)
C(OK,0)
Sending window
Data.req(b)
D(1,b)
Lost
Not expected seq num,
discarded
Retransmission
timer expires
Sending window is full
0 1 2 3
0 1 2 3
D(1,b)
Data.ind(b)
Data.req(d)
D(3,d)
Data.ind(d)
D(2,c)
Data.ind(c)

## Slide 39: Go-back-n : receiver

## Slide 40: Go-back-n : sender

## Slide 41: Go-back-n : example
A B
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3
Data.req(e)
Data.req(a)
Data.ind(a)
D(0,a)
Data.req(c)
D(2,c)
C(OK,0)
C(OK,0)
Sending window
Data.req(b)
D(1,b)
Lost
Not expected seq num,
discarded
Retransmission
timer expires
Sending window is full
0 1 2 3
0 1 2 3
D(1,b)
Data.ind(b)
Data.req(d)
D(3,d)
Data.ind(d)
D(2,c)
Data.ind(c)

## Slide 42: Question
You implement a go-back-n receiver using 3 bits to encode the sequence number. You have correctly received segment 7 and delivered its content. You now receive a correct segment 0, how do you react ?
  you ignore the segment and send ACK(7)
  you accept the segment, deliver it and send ACK(7)
  you accept the segment, deliver it and send ACK(0)

## Slide 43: Question
Go-back-n is used in a network where all data segments are correctly received, but every second acknowledgement is corrupted. How many data segments will be retransmitted by the sender if it needs to reliably send 20 data segments ?

## Slide 44: Question
Go-back-n is used by a protocol that encodes sequence numbers using 5 bits. What is the largest possible sending window (in segments) ?

## Slide 45: Question
Go-back-n is used in a satellite network with a round-trip-time of 1 sec. What is the minimum sending window (in segments) to fully use a 1 Mbps link using 10.000 bits segments ?

## Slide 46: Agenda
Reliable data transfer over a reliable network
How unreliable is the Internet ?
Reliable data transfer techniques
  The Alternating Bit Protocol
  Go-Back-N
  Selective repeat

## Slide 47: The receive window
Buffer managed by receiver
  Stores segments received out-of-order
    Segments remain in receive window until gaps are filled
Receive window size limits the number of segments that the sender can send without acknowledgements
  Sending window cannot be larger than the other side receive’s window
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14
Forbidden seq. num.
Window
Already delivered
Not yet received
Received

## Slide 48: Selective repeat
A B
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3
Data.ind(b)
Data.req(a)
Data.ind(a)
D(0,a)
0 1 2 3
Data.req(c)
D(2,c)
C(OK,0)
C(OK,0)
Sending window
Data.req(b)
D(1,b)
Lost
Segment stored
D(1,b)
Retransmission timer expires
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3
0 1 2 3
Data.ind(c)
Data.req(d)
D(3,d)
Data.ind(d)
0 1 2 3
0 1 2 3
C(OK,2)
C(OK,3)
Rec. window
0 1 2 3
0 1 2 3

## Slide 49: Buffer management
A reliable transport serves a variable number of applications with a limited buffer
  The buffer/window allocated to a given connection may need to change dynamically as connections start and stop

## Slide 50: Buffer management
A B
Data.req(a)
Data.ind(a)
D(0,a)
C(OK,0, w=1)
C(OK,0,w=3)
Data.req(c)
D(2,c)
2 new buffers become available
Data.req(b)
Data.ind(b)
D(1,b)
0 1 2 3
0 1 2 3
0 1 2 3
C(OK,1,w=3)
Rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Swin=3, rwin=1
Swin=3, rwin=3
0 1 2 3
Data.req(d)
D(3,d)
0 1 2 3

## Slide 51: Buffer management
A B
Data.req(b)
Data.ind(a)
Data.req(a)
D(0,a)
C(OK,0, w=0)
2 new buffers are
available
0 1 2 3
Rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Receiver cannot handle segment immediately
C(OK,0,w=3)
Lost segment
0 1 2 3
Swin=3, rwin=0
Window blocked No transmission possible
Waits for control segment
Waits for data segment
How to recover from this deadlock ?
Persistence timer on receiver, resend control segment after timer expiration

## Slide 52: Bidirectional transfer
How to efficiently carry data in both directions ?

## Slide 53: Piggybacking
A B
Data.req(a)
Data.ind(a)
D(0,0,a)
Data.req(b)
D(1,0,b)
Error
Discarded
Data.req(c)
D(2,0,c)
Segment -> buffer
Retransmission
Data.ind(b)
D(1,5,b)
Data.ind(c)
Data.req(d)
D(3,6,d)
Data.ind(d)
C(OK,2)
C(OK,3)
Data.req(x)
D(5,0,w)
Data.req(w)
Data.ind(w)
D(6,0,x)
Data.ind(x)
D(5,0,w) acks D(0,0,a)

## Slide 54: Bytestream
How to provide a bytestream service ?

## Slide 55: Byte stream service (2)
A B
Data.req(ijkl)
Data.req(mnop)
Data.req(abcdef)
Data.ind(ab)
D(0,ab)
C(OK,1)
C(OK,1)
D(2,cd)
Lost segment
D(4,ef)
Placed in buffer
Data.ind(cdef)
D(2,cd)
Expiration timer
Retransmission
D(6,ijklmnop)
Data.ind(ijklmnop)
C(OK,5)
C(OK,13)

## Slide 56: Take back lessons
Usage of Checksums/CRCs
Finite State Machines
Cumulative acknowledgements
Bandwidth x delay product