## Slide 1: Part 8 iBGP and Segment Routing
© O. Bonaventure, UCLouvain, 2023. Supplementary material for the Computer Networking : Principles, Protocols and Practice ebook, https://www.computer-networking.info

## Slide 2: Agenda
Interdomain Routing
  iBGP
Segment Routing

## Slide 3: BGP in large networks
What happens when a network contains tens, hundreds or thousands of routers ?
AS1
AS2
AS3
AS4

## Slide 4: How to distribute BGP routes in a large network ?
AS1
AS2
AS3
eBGP
iBGP

## Slide 5: IP addresses used on routers
AS1
AS2
AS3
A /64 prefix belonging
to the AS1, 2001:11:1:/64
A /64 prefix belonging
to AS2, e.g. 2001:222:12:/64
A /64 prefix belonging
to AS1, e.g. 2001:222:11:13:/64

## Slide 6: A closer look at the BGP messages
AS1
AS2
2001:222:11:13::33
Prefix: p
AS Path : AS3
BGP Nexhop : 2001:222:11:13::33
AS3
Prefix: p
AS Path : AS3
BGP Nexhop : 2001:222:11:13::33
Prefix: p
AS Path : AS1:AS3
BGP Nexhop : 2001:222:12::1234
2001:222:12::1234
p

## Slide 7: Endpoints of the eBGP sessions
eBGP sessions are TCP connections established between the IP addresses of the two routers on the peering link
AS1
AS2
2001:222:11:13::33
AS3
2001:222:12::1234
2001:222:12::5678

## Slide 8: How to distribute BGP routes in a large network ?
Full mesh of iBGP sessions
  Why ?

## Slide 9: Draw iBGP sessions in AS1
AS1
AS2
AS3
AS4
iBGP session

## Slide 10: Endpoints of the iBGP sessions
A router has several IP addresses, on which address should an iBGP session terminate ?
  Any IP address belonging to the router
    Address is associated to an interface, if the interface stops, iBGP session stops as well even if the router is still reachable over other interfaces
  A loopback address
    A software only interface that is always up and announced through the intradomain routing protocol so that it remains reachable as long as the router has one interface up
    Best Current Practice

## Slide 11: How to deal with routers that are not connected to other ASes ?
Run BGP on these routers
Include them in iBGP full-mesh
AS1
AS2
AS3

## Slide 12: How to deal with routers that are not connected to other ASes ?
Make sure that they wlll never have to forward a packet to an external destination
MPLS
AS1
AS2
AS3

## Slide 13: What are the roles of the IGP ?
The intradomain routing protocol distributes information about the reachability of :
  IP prefixes associated to internal links between routers of the AS
  IP addresses associated to loopback interfaces or routers of the AS
  IP prefixes associated to peering links between a router of this AS and another AS

## Slide 14: BGP Nexthop self
Helps to reduce # routes in the IGP
AS1
AS2
2001:222:11:13::33
AS3
Prefix: p
AS Path : AS3
BGP Nexhop : 2001:11:1001::1
Prefix: p
AS Path : AS1:AS3
BGP Nexhop : 2001:222:12::1234
2001:11:1001::2
Prefix: p
AS Path : AS3
BGP Nexhop : 2001:222:11:13::33
2001:11:1001::1
2001:222:12::1234

## Slide 15: The BGP decision process
Ignore routes having an unreachable BGP nexthop
Prefer routes having the highest local-pref
Prefer routes having the shortest AS-Path
Prefer routes having the smallest MED
Prefer routes learned via eBGP sessions over routes learned via iBGP sessions
Prefer routes having the closest next-hop
Tie breaking rules : prefer route learned from the router with lowest router id

## Slide 16: 1st step of BGP decision process
1. Ignore routes having an unreachable BGP nexthop
  Why would a BGP route contain an unreachable nexthop ?

## Slide 17: Unreachable nexthop
Usually a transient issue
AS1
AS3
AS2

## Slide 18: 2nd step of BGP decision process
2. Prefer routes having the highest local-pref
  Implement routing policies
    Prefer customer routes over shared-cost and provide routers
  Support backup routes
Local-pref attribute to added by the import filter on eBGP session and distributed to all routers over iBGP sessions

## Slide 19: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p
local-pref=50
local-pref=99
Path towards p

## Slide 20: 3rd step of BGP decision process
3. Prefer routes having the shortest AS-Path
  Some operators believe that a BGP route with a long AS Path has a lower performance than a route with a longer AS Path
    This is not always true…

## Slide 21: 5th step of BGP decision process
5. Prefer routes learned via eBGP sessions over routes learned via iBGP sessions
  Motivation : Hot potato routing
    Routers should try to forward packets towards external destinations to another AS a quickly as possible

## Slide 22: 6th step of BGP decision process
6. Prefer routes having the closest next-hop
  Motivation : Hot potato routing
    Routers should try to forward packets towards external destinations to another AS a quickly as possible

## Slide 23: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p
Path towards p

## Slide 24: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p
AS2
AS3
AS5
Path towards p

## Slide 25: 4th step of BGP decision process
Prefer routes having the smallest MED
MED means Multi-Exit Discriminator
  Motivation : Cold potato routing
  Enable neighbour AS (usually customer) to indicate the best peering link to reach a given prefix

## Slide 26: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p
MED=50
MED=99
Path towards p

## Slide 27: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p
AS2
AS3
MED=IGP
MED=IGP
MED=IGP
MED=IGP
IGP=7
IGP=2
Path towards p

## Slide 28: 7th step of the BGP decision process
7. Tie breaking rules : prefer route learned from the router with lowest router id
  Motivation : select a single best route towards each destination prefix
    This best route is the route that can be advertised over eBGP session
  Note that recent routers sometimes load balance (BGP Multipath) the traffic towards a given prefix over several routes (having the same BGP attributes)

## Slide 29: Differences between iBGP and eBGP
  Which routes are advertised by a router over iBGP and eBGP sessions ?
    Over an eBGP session, a router advertises its best route towards each destination prefix
      Provided this advertisement is allowed by the export filter
      At most one route per destination prefix
    Over an iBGP session, a router advertises its best route towards each destination prefix provided that this best route was learned over an eBGP session
      Since iBGP sessions are in full-mesh, there is no need to readvertise a route learned over another iBGP session

## Slide 30: Differences between iBGP and eBGP
  Which filters are used over iBGP and eBGP sessions ?
    Import and export filters are used over all eBGP sessions
      Usually, there is a series of import filters attached to each peering link
      Filters are usually implemented as modules that are combined together and associated to similar peering links (e.g. customer filter, provider filter, …)
    No filter is applied on iBGP sessions

## Slide 31: Which BGP routes are known ?
AS1
AS2
AS3

## Slide 32: Differences between iBGP and eBGP
  What are the attributes carried by iBGP and eBGP
    Prefix : iBGP and eBGP
    AS Path : iBGP and eBGP
      AS Path is updated when a BGP message is sent over an eBGP session
    Local-pref : iBGP
      Local-pref cannot be used on eBGP sessions
    MED : iBGP and eBGP
    Nexthop : iBGP and eBGP
      Nexthop is updated when a BGP message is sent over an eBGP session

## Slide 33: What happens if iBGP sessions are missing ?
AS1
R1
AS4
R4
R5
R6
p
AS2
AS3
AS5
IGP=7
Path towards p

## Slide 34: What happens if iBGP sessions are missing ?
AS1
R1
AS4
R4
R5
R6
p
AS2
AS3
AS5
Path towards p

## Slide 35: What happens if iBGP sessions are missing ?
AS1
R1
AS4
R4
R5
R6
p
AS2
AS3
AS5
Path towards p

## Slide 36: Conclusion
BGP depends on the underlying intradomain routing protocol
  Establishment of the iBGP sessions
  Resolution of the BGP nexthop
iBGP and eBGP play different roles
  eBGP over sessions with routers in other ASes
  iBGP sessions (in full mesh) inside an AS
The BGP decision process ranks routes
  Hot potato versus cold potato routing

## Slide 37: Reading list
  1st edition, BGP section http://cnp3book.info.ucl.ac.be/network/network/#the-border-gateway-protocol

## Slide 38: Agenda
Interdomain Routing
  iBGP
Segment Routing

## Slide 39: IPv6 Segment Routing
Objectives
  Allow operators to use non-shortest paths inside their networks using Source routing paradigm
  Provide advanced services
    Traffic engineering
    Middleboxing
See http://www.segment-routing.org and http://www.segment-routing.net

## Slide 40: Source routing
Each packet contains intermediate nodes
R1
R2
R4
R5
R6
R3
R7
R8
R9
RD
RD via R5,R4
RD via R5,R4
RD via R5,R4
RD via R5,R4
RD via R5,R4
RD via R5,R4

## Slide 41: What is a segment ?
An IPv6 address that identifies
  A router in the network (node)
    Advertised by the routing protocol
  An outgoing link on a router
    Advertised by the routing protocol
    Can be used to realise specific paths
  An abstract service (e.g. firewall)

## Slide 42: IPv6 SR Header
32 bits
NxtHdr HLen
RType SLeft
Segment List[0]
Segment List[1]
First Flags Res.
Segment List[n]
Number of segments left. Pointer in address list
Type Length Res.
HMAC Key ID
HMAC (32 bytes)
Notes: The Type 0 Routing header is specified in RFC2460
Two other types of routing headers have been defined. Type 1 is experimental and never used. Type 2 is specific for Mobile IPv6 that will be covered later.

## Slide 43: SR capable host
Endhost
  Adds SR header to each transmitted packet
  HMAC allows network to check endhost is using a valid segment list

## Slide 44: IPv6SR Example
2001:6a8:3080:4::d
R1
R
R
R3
R
2001:6a8:3080:1::a
2001:6a8:3080:1::a
2001:6a8:3080:3::FF
R2
2001:6a8:3080:22::CC
R
R
NxtHdr HLen
RType 1
2001:6A8:3080:22::CC
Reserved
SRC: 2001:6A8:3080:1::A
2001:6A8:3080:4::D
2001:6A8:3080:22::CC
NxtHdr HLen
RType 0
2001:6A8:3080:22::CC
Reserved
SRC: 2001:6A8:3080:1::A
2001:6A8:3080:4::D
2001:6A8:3080:4::D